## Slide 1
eXPERIMENTAL STUDY ON LANE CHANGe maneuvers WITH A mOTORCYCLE
Horst Ecker
Stefan Litschauer
TU-Wien
Vienna University of Technology
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 2
eXPERIMENTAL STUDY ON LANE CHANGe maneuvers WITH A mOTORCYCLE
Horst Ecker
Stefan Litschauer
TU-Wien
Vienna University of Technology
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 3
The Goal
The Method
The Result
A generic mathematical model of the lane change maneuver for dynamic studies and control purposes.
Measuring dynamics data using an intrumented motorcycle and conducting riding experiments.
Data mining and a heuristic approach leads to a parameterized mathematical model.
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany
Litschauer / Ecker – Experimental and theoretical study on motorcycle lane change maneuvers
Extra results
Reaction time measurements were carried based on an external visual trigger signal.

## Slide 4
The Goal
The Method
The Result
A generic mathematical model of the lane change maneuver for dynamic studies and control purposes.
Measuring dynamics data using an intrumented motorcycle and conducting riding experiments.
Data mining and a heuristic approach leads to a parameterized mathematical model.
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany
Extra results
Reaction time measurements were carried based on an external visual trigger signal.

## Slide 5
Two Riders - One Motorcycle
SL
HE
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 6
Urban roads
Country roads
Highways
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 7
Country roads
Highways
Urban roads
Known distance
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 8
Country roads
Highways
Urban roads
Driving Path
max. 130 km/h
max. 50 km/h
max. 100 km/h
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 9
Speed range covered by experiments
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 10
The Probe Vehicle
Motion Signals (displacement, angles, velocities, accelerations, wheel speeds, etc.)
Vehicle signals (engine speed, throttle position, brake pressure, etc.)
Position signals (GPS-data)
Video signals (Two on-board cameras)
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 11
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 12
The Goal
The Method
The Result
Extra results
A generic mathematical model of the lane change maneuver for dynamic studies and control purposes.
Measuring dynamics data using an intrumented motorcycle and conducting riding experiments.
Data mining and a heuristic approach leads to a parameterized mathematical model.
Reaction time measurements were carried based on an external visual trigger signal.
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 13
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany
Lateral diplacement – Lane change to the left @ 52 km/h
Lateral acceleration – Lane change to the left @ 52 km/h

## Slide 14
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany
Yaw rate– Lane change to the left @ 52 km/h
Roll angle (blue) / Roll rate (red) – Lane change to the left @ 52 km/h

## Slide 15
High Intensity lane change @ 79 km/h (49 mph)
Low Intensity lane change @ 58 km/h (36 mph)
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 16
Time series of roll angles of all measured lane change maneuvers at all speeds, synchronized by the zero crossing of the roll angle approximately in the middle of the lane change.
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 17
Histogram of maximum roll angle at low speeds of both riders; blue (HE) red (SL)
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany
Notes: .

## Slide 18
Roll Angle (deg)
Histogram of roll angle at all speeds of both riders; orange (HE+SL @ low speed), blue (high speed)
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 19
Histogram of roll angle at all speeds of both riders; orange (HE+SL @ low speed), blue (high speed)
Histogram of the roll rate at all speeds of both riders; orange (HE+SL @ low speed), blue (high speed)
Roll Angle (deg)
Roll Rate (deg/s)
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 20
Dependency of the lane change duration on the maximum roll angle
Speed versus maximum roll angle for full lane changes
High speed 
Half lane ch. 
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 21
Data Mining Results
I … „Intensity“ [-] (agressivity/ambition) of the lane change execution, defined for a range of [0 …10]
… Max. Roll Angle [deg] reached during a lane change
= Duration [sec] of a lane change maneuver
b … Width [m] of the lane change
…Max roll rate [deg/s] reached in an lane change
… Analytic expression for the time history of the roll rate as a function of the most siginificant parameters
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 22
High Intensity lane change @ 79 km/h (49 mph)
Low Intensity lane change @ 58 km/h (36 mph)
Comparison of measured and synthetic signals
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 23
The Goal
The Method
The Result
Extra results
A generic mathematical model of the lane change maneuver for dynamic studies and control purposes.
Measuring dynamics data using an intrumented motorcycle and conducting riding experiments.
Data mining and a heuristic approach leads to a parameterized mathematical model.
Reaction time measurements were carried based on an external visual trigger signal.
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 24
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany
Micro-Switch
to
detect steering action
Visual signal activated by car driver is recorded by on-board cameras
Steering
Action
Reaction
Time
Measure-ments

## Slide 25
Test Series | n | x̅ | x̃ | σ | MIN | MAX
HE1 | 16 | 0,83 | 0,77 | 0,35 | 0,27 | 1,58
HE2 | 20 | 0,74 | 0,58 | 0,32 | 0,46 | 1,47
SL1 | 16 | 0,53 | 0,50 | 0,16 | 0,34 | 0,85
HE | 36 | 0,78 | 0,69 | 0,33 | 0,27 | 1,58
SL | 16 | 0,53 | 0,50 | 0,16 | 0,34 | 0,85
Total | 52 | 0,70 | 0,61 | 0,31 | 0,27 | 1,58
Statistical parameters of the „Steering Reaction Time“
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 26
The Summary
The Outlook
A generic mathematical model of the lane change maneuver was developed.
As the most influencial parameters, the maneuver „intensity“, the width of the lane change and the max. roll rate were identified.
Further riding experiments will be carried out to collect more data and to verify the results.
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany

## Slide 27
The authors are grateful to KTM Motorcycles Inc. for providing the motorcycle used in this study.
The authors would like to thank Manfred Neumann for his valuable help when carrying out the measurements.
Thank you for your interest and attention !
13th International Motorcycle Conference, Sept 1 – Oct 6, 2020, IFZ, Essen, Germany